## Slide 1: SHIP++: Enhancing Signature-Based Hit Predictor for Improved Cache Performance
Vinson Young, Georgia Tech
Chia-Chen Chou, Georgia Tech
Aamer Jaleel, NVIDIA
Moinuddin K. Qureshi, Georgia Tech
CRC-2, ISCA 2017
Toronto, Canada
June 25, 2017
Notes: 25 minutes total per slot.
20 minute presentation, 4 minute question, 1 minute change.

## Slide 2: Importance of Replacement Policy
  Increasing # of cores increase memory load
  Improving cache hit rate reduces memory load for cheap
    Improve access latency  improves performance
    Reduce memory accesses  improves power and performance
  LRU is commonly used

## Slide 3: Problems with LRU Replacement
  Working set larger than the cache causes thrashing
  References to non-temporal data (scans) discards frequently referenced working set
miss
miss
miss
miss
miss
hit
hit
hit
miss
hit
miss
miss
scan
scan
scan
Wsize
Wsize
  scans occur frequently in commercial workloads
LLCsize
LLCsize
Notes: The first problem with LRU replacement is when the working set is larger than the cache. In such scenarios, LRU causes cache thrashing and always results in misses!
The second problem is when references to non-temporal data, called scans, discards the frequently referenced working set from the cache. Let me illustrate. When the working set is smaller than the LLC it receives cache hits. Successive references to the working set continue to receive cache hits. However, after a one-time reference to a long stream of data, re-references to the working set after the scan result in a miss under LRU replacement. Successive re-references after re-fetching the data from memory result in hits until the next scan. And the problem repeats . After every scan, the frequently referenced working set always misses!
Why is this important? Well, our studies show that scans occur frequently in many commercial workloads.
-wu

## Slide 4: Desired Behavior from Cache Replacement
hit
hit
hit
hit
hit
miss
miss
miss
miss
miss
  Working set larger than the cache  Preserve some of working set in the cache
  Recurring scans  Preserve frequently referenced working set in the cache
hit
hit
hit
hit
scan
scan
scan
hit
hit
hit
Wsize
LLCsize
[ DIP (ISCA’07), DRRIP (ISCA’10) achieves this effect ]
[ SRRIP (ISCA’10) achieves this effect ]
Notes: Under both these scenarios, the desired behavior from cache replacement is as follows:
If working set is larger than cache, preserve some of it in the cache.
In the presence of recurring scans, the replacement policy should preserve the frequently referenced working set in the cache.
-wu

## Slide 5: Dynamic Re-Reference Interval Prediction ( DRRIP )
0
Imme-
diate
1
Inter-
mediate
2
far
3
distant
re-reference
No Victim
insertion
re-reference
eviction
re-reference
No Victim
No Victim
(SRRIP)
Scan-Resistant
[ Jaleel et al., ISCA’10 ]
insertion
( BRRIP )
Thrash-Resistant
Notes: Since our work builds on top of the re-reference interval framework, I would like to quickly review the RRIP replacement policy. Like LRU which holds the LRU position with each cache line, RRIP replaces the notion of the “LRU” position with a prediction of the likely re-reference interval of a cache line. For example, with 2-bit RRIP, there are four possible re-reference intervals. If a line has re-reference interval 0, it implies the line will be re-referenced soon. If a line has re-reference interval 3, it implies the line will be re-referenced in the distant future. In between distant and immediate there is intermediate and far re-reference intervals.
When selecting a victim, RRIP always selects lines that have a distant re-reference interval for eviction. If no line is found, the states of all lines in the set are incremented until a line with distant re-reference interval is found.
When inserting new lines in the cache, scan-resistant SRRIP dynamically tries to learn the re-reference interval of a line by initially inserting ALL lines with “far” re-reference interval. This is done in an effort to dynamically learn the blocks re-reference interval. If the line has no locality, it will be quickly discarded. However, if the line has locality, on the next re-reference the line is moved to have immediate state, hence preserving it in the cache for a longer time.
-wu

## Slide 6: Dynamic Re-Reference Interval Prediction ( DRRIP )
0
Imme-
diate
1
Inter-
mediate
2
far
3
distant
re-reference
No Victim
insertion
re-reference
eviction
re-reference
No Victim
No Victim
(SRRIP)
Scan-Resistant
[ Jaleel et al., ISCA’10 ]
insertion
( BRRIP )
Thrash-Resistant

## Slide 7: Signature-based Hit Predictor (SHiP)
0
Imme-
diate
1
Inter-
mediate
2
far
3
distant
re-reference
No Victim
insertion
re-reference
eviction
re-reference
No Victim
No Victim
PC-classified
Re-use
[ Wu et al., MICRO’11 ]
insertion
PC-classified
Scan

## Slide 8: Observe Signature Re-Reference Behavior
  Observe re-reference pattern in the baseline cache
Cache Tag
Replacement State
Coherence State
LLC
Load/Store
Address

## Slide 9: Observe Signature Re-Reference Behavior
  Observe re-reference pattern in the baseline cache
  Gathering Signature:
    Was line re-referenced after cache insertion ( 1-bit )
    “Signature” responsible for cache insertion ( 14-bits )
LLC
reuse bit
signature_insert
Signature
Load/Store
Address
metadata

## Slide 10: Learn Signature Re-Reference Behavior
  Learn signature re-reference behavior
  Signature History Counter Table (SHCT)( 16K, 3-bit counters )
SHCT
Cache Hit 
SHCT[signature_insert]++
Evict (re-use=0) 
SHCT[signature_insert]--
000
SHCTR
Non-zero
Learning with SHCT

## Slide 11: Predicting Signature Re-Reference Behavior
  Learn signature re-reference behavior
  Signature History Counter Table (SHCT)( 16K, 3-bit counters )
SHCTR = 0, predict
NOT re-referenced.
Install state=3
SHCT
000
SHCTR
Non-zero
SHCTR != 0, predict
signature re-referenced.
Install state=2
Predicting with SHCT
Notes: Leverage SHCT to improve confidence of install

## Slide 12: SHiP Improvements
  3 improvements under no-prefetching
    High-Confidence Install
    Balanced SHCT Training
    Write-back-aware Install
  2 improvements under prefetching
    Prefetch-aware Training
    Prefetch-aware State-Update

## Slide 13: Improvement 1: High-Confidence Installs
Previous: SHiP always installs with state 2 or 3
Observation: RRIP requires re-use before promoting to state 0.
But, some workloads benefit from keeping re-use lines longer
Solution: Leverage SHCT to confidently install at state 0.
Install with state 0, when SHCTR saturated at 7
Notes: Leverage SHCT to improve confidence of install

## Slide 14: Improvement 1: High-Confidence Installs
0
Imme-
diate
1
Inter-
mediate
2
far
3
distant
re-reference
No Victim
insertion
re-reference
eviction
re-reference
No Victim
No Victim
Re-use
0 < SHctr < 7
[ Jaleel et al., ISCA’10 ]
insertion
Scans
SHCtr == 0
insertion
High-confidence
SHCtr == 7
Notes: Insight: Keep high confidence lines longer

## Slide 15: Improvement 2: Balanced SHCT Training
Previous: SHCT Learns on all hits and evictions
Observation: Small number of high-access-frequency lines saturate CTRs (mcf and sphinx)
Solution: Learn from only first-hit and evictions

## Slide 16: Improvement 2: Balanced SHCT Training
SHCT
Cache Hit (re-use=0) 
SHCT[signature_insert]++
Evict (re-use=0) 
SHCT[signature_insert]--
000
SHCTR
Non-zero
Learning with SHCT

## Slide 17: Improvement 3: Writeback-Aware Installs
Previous: No differentiation for Writebacks
Observation: Writebacks not in critical path and signal end of a context. Can be bypassed.
Solution: Install writebacks at state 3 (why? Model requires install of writebacks)

## Slide 18: Improvement 3: Writeback-Aware Installs
0
Imme-
diate
1
Inter-
mediate
2
far
3
distant
re-reference
No Victim
insertion
re-reference
eviction
re-reference
No Victim
No Victim
Re-use
0 < SHctr < 7
[ Jaleel et al., ISCA’10 ]
insertion
Scans + Writebacks
(SHCtr == 0) || is_wb
insertion
High-confidence
SHCtr == 7
Notes: Insight: Keep high confidence lines longer

## Slide 19: Results (under no prefetching)
  SHiP++ achieves 6.2% Speedup over LRU (SHiP is 3.9%)
38
64
26
Notes: High-confidence installs
Helps calculix, Gems, zeusmp
Better SHCT training (first-hit + eviction)
Helps mcf and sphinx

## Slide 20: Improvement 4: Prefetch-Aware Training
Previous: No differentiation for Prefetches
Observation: Demand may have re-use, but prefetched lines may not have re-use
Solution: Learn separately in different halves of SHCT.
Use Signature = (PC << 1) + is_pf

## Slide 21: Improvement 4: Prefetch-Aware Training
SHCT
Cache Hit (re-use=0) 
SHCT[signature<<1 | is_pf]++
Evict (re-use=0) 
SHCT[signature<<1 | is_pf]--
000
SHCTR
Non-zero
Learning with SHCT
SHCTR
Prefetch half of SHCT
Demand half of SHCT

## Slide 22: Improvement 4: Prefetch-Aware Training
Cache Hit (re-use=0) 
SHCT[signature<<1 | is_pf]++
Evict (re-use=0) 
SHCT[signature<<1 | is_pf]--
000
SHCTR
Non-zero
Learning with SHCT
SHCTR
Predict re-use for prefetch, separately
Predict re-use
Predicting with SHCT

## Slide 23: Improvement 5: Prefetch-Aware State-Update
Previous: No differentiation for Prefetch
Observation: Prefetches are staying in caches for a long time. First-access to prefetched line is demand access. Baseline SHiP promotes and keeps accurate prefetches past usefulness
Solution: Ignore state-update for first access to prefetched line. Update for subsequent accesses

## Slide 24: Improvement 5: Prefetch-Aware State-Update
0
Imme-
diate
1
Inter-
mediate
2
far
3
distant
re-reference && ! is_pf
insertion
re-reference && ! is_pf
eviction
re-reference && ! is_pf
No Victim
No Victim
Re-use
0 < SHctr < 7
[ Jaleel et al., ISCA’10 ]
insertion
Scans + Writebacks
(SHCtr == 0) || is_wb
insertion
High-confidence
SHCtr == 7
No Victim
On first-access to prefetched:
unset is_pf;
no state-update;
Notes: Insight: Keep high confidence lines longer

## Slide 25: Results (under prefetching)
  SHiP++ achieves 4.6% Speedup over LRU (SHiP is 2.3%)
21
65
Notes: Sphinx and mcf.
Learns their prefetches are not accurate and installs them at low priority.

## Slide 26: Summary
  SHiP++: improve PC-based classifier for re-use / no-re-use PC’s
    High-Confidence Install
    Balanced SHCT Training
    Write-back-aware Install
    Prefetch-aware Training
    Prefetch-aware State-Update
  6.2 % speedup (base config), 4.6 % speedup (prefetch config)

## Slide 27: THANK YOU