## Slide 1: ReD: A Policy Based on Reuse Detection for Demanding Block Selection in Last-Level Caches
Javier Díaz1, Pablo Ibáñez1, Teresa Monreal2,
Víctor Viñals1 and José M. Llabería2
1 Aragón Institute of Engineering Research (I3A), University of Zaragoza, and Hipeac
2 Departament d'Arquitectura de Computadors, Universitat Politècnica de Catalunya and Hipeac

## Slide 2: Basic ideas
A block selection / bypass policy
  Can be combined with any other insertion, promotion and victim selection algorithms
Demanding
  Blocks classified dead on arrival and bypassed by default
Reuse-based. Blocks are stored only
  if reuse is detected: the second time they are requested
  or if their requesting instruction has shown to request highly-reused blocks

## Slide 3: A block selection / bypass policy
Without selection, most blocks are not requested again from the LLC after they are stored
Selection has major potential
Approach
  Focus in block selection as a separate problem
  Enable combination with other components of the replacement policy

## Slide 4: Demanding Reuse-based approach
  Most blocks are not requested again from the LLC after they are stored
    By default: blocks classified dead on arrival and bypassed
Blocks accessed at least twice tend to be reused many times
    Our main goal: to detect the second request to a block
    We need to remember addresses of requests that have recently missed in the LLC
Inspired in the Reuse Cache (Albericio et al.)

## Slide 5: Address Reuse Table (ART)
    Remembers addresses that have recently missed in the LLC
  Miss in ART  first request to a block  bypass LLC, insert into ART
  Hit in ART  second or later request to a block  store block in LLC
    Each ART is a set-associative buffer
      Separated from the LLC
        Unaffected by decisions of the base replacement policy
        More simple to implement
      Private for each core
        Increases fairness of the reuse detection between threads
        Diminishes inter-core thrashing in the LLC

## Slide 6: The need for a secondary mechanism
Using only the ART a block with reuse experiences two LLC misses
To avoid one miss  predict the reuse pattern at the initial request
Secondary mechanism
  Detects instructions that request highly-reused blocks
  Enables storing blocks requested by those instructions at their initial request
  Requires remembering the past behavior of instructions and blocks  requires the ART

## Slide 7: Program Counter - Reuse Table (PCRT)
Tracks the reuse of blocks requested by each instruction (PC)
Two counters per entry: #reused and #notreused
  They keep the number of addresses that a PC inserts in ART and are finally reused or not
A PC with reuse probability higher than ¼ sends all initial requests to the LLC
PCRT also used to reduce the insertion of addresses in ART
  PCs with reuse probability very high (>¼) or very low (<1/64) only insert 1 in 8 times

## Slide 8: ART and PC-RT entries
ART
  Indexed by block address
  One entry tracks 4 blocks
  PAt: Partial Address tag
  4 valid bits
ART with PC indexes
  4 PC indexes
PCRT
  Tagless
  Indexed by 8 bits of the PC
  Two 10-bit counters

## Slide 9: Example
State of ReD internal tables after two initial requests (1) (2), and a first-reuse request (3). ART set shown uses PC sampling

## Slide 10: Other details
Base replacement policy: 2-bit SRRIP
  On insertion, only applied if ReD decides not to bypass
  We also tried with 3p-4p with similar results
No distinction between prefetch and demand requests
Write-back requests
  Ignored by ReD
  If they miss, they are allocated in the LLC but with minimum priority

## Slide 11: Results: speedup in single-core configs
1.044
1.024

## Slide 12: Results: speedup in multi-core configs
1.056
1.036

## Slide 13: Results: bypass rate (c1)

## Slide 14: Thank you

## Slide 15: Backup

## Slide 16: ART details
    One ART per core
Set-associative buffer with 16 ways and 512 sets
FIFO replacement policy
Partial address tags, 11 bits
An entry tracks four consecutive LLC blocks
Four valid bits per entry
15616 bytes per core

## Slide 17: PCRT details
PCRT is tagless and has 256 entries
  Indexed by 8 bits of the trigger PC
Two 10-bit counters per entry
  When a counter reaches its maximum, both counters of the entry are divided by two
We need to store in ART the PC that requests each address
  Set sampling in ART: only ¼ of the ART entries include PC information
640 bytes per core
8192 bytes per core